## Slide 1: Universal Ground Station Receiver for Hubsan X4 PDR
Johns Hopkins
Engineering for Professionals
Kyle Mercer – 02/12/18

## Slide 2: Description
Universal Ground Station Receiver
  Listens for incoming Bluetooth© signals
  Re-broadcasts controls in Hubsan’s format
Virtually any Bluetooth slave can become a transmitter, including:
  Your PC
  Your smartphone
  Corrie’s glove controller project
Hubsan X4

## Slide 3: Description (cont.)
Capabilities
  Command translation and relay for Quadcopter control
  Any Bluetooth slave may pair
  Universal control packet scheme
  “Training” Mode for new users
Limitations
  Only Bluetooth protocol support
  Single Quadcopter brand supported
  Single transmitter per session (feature?)
  Only A7105 RF chip support (Quadcopter comms)
Ground Station

## Slide 4: Functional Description (Overall)

## Slide 5: Functional Description (Ground Station)
A7105 2.4 GHz Receiver
(Hubsan X4 H107L)
A7105
2.4 GHz Transmitter
(2.0-3.6V)
Bluetooth
Receiver
Ground Station
5V
ATmega328P (16 MHz)
Hubsan X4 (H107L)
Common Derived Protocol
Level Shifter
5V→ 3.3V
Common Derived Protocol
5V
3.3V
UART
(RX/TX)
115200 baud
Protocol Parser
Translation Layer
Bluetooth UART Interface
A7105 SPI Interface
SPI
(SCK, MISO, MOSI, SS)
8 Mbps
2
/
4
/
4
/
RST
Training Mode
Btn
Wireless
Wired
3.7V
…

## Slide 6: Materials & Resources
Hardware | Software | Test Equipment
ATmega328P AVR MCU COTS Hubsan X4 (H107L) Quadcopter 9V/3.7V LiPo batteries 5V regulator Capacitors/Resistors Prototyping board Insulated proto wires A7105 Wireless RF 2.4GHz Transceiver Module Bluesmirf Bluetooth modem (RN-42) 5V to 3.3V level shifter | Linux dev environment Arduino CLI toolchain AVR compiler SPI UART Collaboration tools Git Google cloud | Arduino Uno/Mega FTDI AVR programmer Volt meter Oscilloscope Breadboard Prototyping wires LiPo battery charger
Lead-time on hardware
  A7105 RF module: 7–20 days (already obtained from eBay)
  Everything else: 2–5 days (Thanks Amzn!)

## Slide 7: Materials & Resources (cont.)
Group project logistics
Project Partner: Corrie Russell
  Expected from me
    Common (Bluetooth) protocol ICD
    Ground station deliverable to be used with controllers
  Expected from Corrie’s project
    Traditional style transmitter (double joystick)
    Glove controller transmitter
    Both controllers implement common protocol

## Slide 8: Schedule
Task # | Objective
1 | Design and finalize Common Bluetooth Protocol ICD for handoff
2 | Implement Bluetooth receiver interface
3 | Implement common protocol processing interface
4 | Create A7105 SPI interface for Hubsan comms
5 | Establish communication with Hubsan Quadcopter (binding phase)
6 | Implement translation layer
7 | Implement “training mode” feature
8 | Integrate tasks 2 through 7 into higher level system
9 | Test full system with Glove/traditional controller driving control data
10 | Final ruggedized hardware assembly
*Meeting point with Corrie’s project

## Slide 9: Risks & Mitigation Plan
Risk | Mitigation Plan
Development of Common Protocol | Protocol development task 1st in schedule Allocate more time task if risk is realized.
Binding to COTS Hubsan Quadcopter with A7105 RF module | Move binding task up on schedule Use existing transmitter as surrogate for binding procedure with MCU if risk fully realized
Program flash memory of ATmega328P (32KB) insufficient | Move to ATmega2560 (256KB) Low impact if risk is realized

## Slide 10: References
Hubsan X4 reversed protocol specification
  http://www.jimhung.co.uk/wp-content/uploads/2014/11/HubsanX4_ProtocolSpec_v1.txt
  http://www.jimhung.co.uk/?p=1349
Deviation10 firmware (targets 32-bit ARM)
  https://bitbucket.org/PhracturedBlue/
Bluetooth modem RN-42 AT command set
  https://cdn.sparkfun.com/datasheets/Wireless/Bluetooth/bluetooth_cr_UG-v1.0r.pdf
Atmel’s AVR documentation
  http://www.microchip.com/wwwproducts/en/ATmega328p
ATmega328P standalone assembly
  https://www.arduino.cc/en/Main/Standalone

## Slide 11: BACKUP SLIDES

## Slide 12: Interfaces
Standard Interfaces
  Bluetooth interface
    Universal Async RX/TX (UART)
    TX & RX
    115200 baud
  A7105 IC interface
    Serial Peripheral Interface (SPI)
    SCK, MISO, MOSI, SS
    8 Mbps (10Mbps max)
Derived Interface
  Universal wireless protocol

## Slide 13: Materials & Resources (cont.)
Lead-time on hardware
  A7105 RF module: 7–20 days (already obtained from eBay)
  Everything else: 2–5 days (Thanks Amzn!)
Knowledge Base
  AVR documentation
  Hubsan X4 reversed protocol specification
    http://www.jimhung.co.uk/wp-content/uploads/2014/11/HubsanX4_ProtocolSpec_v1.txt
  Bluetooth modem RN-42 AT command set
    https://cdn.sparkfun.com/datasheets/Wireless/Bluetooth/bluetooth_cr_UG-v1.0r.pdf

## Slide 14: Development Plan & Schedule
Approach
  Design common Bluetooth protocol
  Design ground station prototype on breadboard
  Breakout board modules (Bluetooth and A7105)
  Implement software unit tests for all interfaces
  Integrate elements into overall system
  Transition hardware over to ruggedized prototyping board